## Example 4:	move an intruder in a 2D granular material
# New tricks: use grains as a boundary, 2D simulation, use group to control particles separately
# Commands that appears in previous examples will not be repeatedly explained.
# More command details in the documentation https://lammps.sandia.gov/doc/Commands.html
# LAMMPS version: LAMMPS (7 Aug 2019) on linux

# change the default dimension to 2
dimension	2
atom_style	sphere
boundary	p p p
newton	off
comm_modify	vel yes

region	reg block -5 5 -5 5 -0.5 0.5 units box
# define a simulation region with 2 particle types
create_box	2 reg

# In the data file, we have randomly positioned particles, which means that they can highly overlap,
# and two intruders of diameter 3.0, one of them is the 32th particle, the other is the 76th particle.
# All the rest are smaller particles (of diameter 1.0 or 1.4) that form the packing.
# their density is 1.0.
# the intruders are of type=2, the rest particles are of type=1
read_data	data add merge

# To separately manipulate particles, we define different groups according to their attributes
# define a group of particles named ‘intruder1’, which contains a particle with ID==32
group	intruder1 id == 32
# define a group of particles named ‘intruder2’, which contains a particle with ID==76
group	intruder2 id == 76
# define a group of particles named ‘packing’, which contains particles with particle type<=1
group	packing type <= 1

fix	1 packing nve/sphere
fix	11 intruder1 nve/sphere
fix	12 intruder2 nve/sphere

neighbor	0.2 bin
neigh_modify	delay 0

pair_style gran/hooke/history 400.0 NULL 10.0 NULL 0.75 1
pair_coeff	* *

timestep	0.001

# just zero out the z-dimension velocity and force on all atoms
fix 2 all enforce2d

compute	ke all ke
compute	re all erotate/sphere

thermo_style	custom step atoms c_ke c_re
thermo	100
thermo_modify	lost warn norm no

dump	2 all image 100 *.jpg type diameter zoom 1.6 view 0 0
dump_modify	2 pad 5

# the first run relax the initial random positioning of the particles,
# so it looks like a packing in the end of this run
run 5000

# exclude interactions between the two intruders
neigh_modify	exclude group intruder1 intruder2

# we remove the effect of the fix command named ‘12’
# the position and velocity of intruder2 will not be updated according to F=ma (i.e. nve)
# That is, intruder2 will no longer move, but used as a fixed boundary
unfix	12

# Add a position-controlled fix to intruder1, so that its velocity is fixed to vx=0.0, vy=0.7,
# and the z direction is not influenced (NULL).
# That is, intruder1’s motion is position-controlled, and the force on it will fluctuates.
fix	hxFix intruder1 move linear 0.0 0.7 NULL
# need to remove the F=ma integration on intruder1, because the two fixes will make the intruder move
# twice during simulations.
unfix	11

# the second run stirs the packing by moving one intruder and fixing the other.
run 10000